## Slide 1: Drilling Cost and Hole Problems
1.5-1

## Slide 2: 1.5-2 The Drilling Cost Equation:
Cf = drilling cost, $/ft Cb= cost of bit, $/bit
Cr= fixed operating cost of rig, $/hr
tb= total rotating time, hrs
tc= total non-rotating time, hrs
tt= trip time (round trip), hrs
= footage drilled with bit, ft
Eq. 1.16
Notes: This is the very often used drilling cost equation, that is used to calculate the cost per foot of hole drilled. It is used in planning to calculate which bits give the lowest cost per foot, to determine when it is most economical to pull a bit that is becoming dull, and to analyze how efficiently the well has been drilled.
Obviously, we want to keep the cost to drill at a minimum – as long as it does not have any detrimental effect on the wells production rate.

## Slide 3: 1.5-3 Drilling Costs
Tend to increase exponentially with depth. Thus, when curve-fitting drilling cost data, it is often convenient to assume a relationship between total well cost, C, and depth, D, given by
C = aebD …………………..(1.17)
Notes: Studies have been to show that costs indeed to increase exponentially with depth. Reasons – harder rock, slower drilling, higher pressures, more mud volume, more casing, larger rigs, more time, etc.

## Slide 4: 1.5-4
Fig. 1-65. Least-square curve fit of 1978 completed well costs for wells below 7,500 ft in the south Louisiana area.
Notes: These plots show the cost of almost 2000 wells drilled below 7500’ in south Louisiana. We show this to emphasize that the cost to drill is very high even when things go right. Well problems can make these costs easily double or triple.

## Slide 5: 1.5-5 Drilling Time cont’d
Plotting depth vs. drilling time from past drilling operations:
A. Allows more accurate prediction of time and cost for drilling a new well
B. Is used in evaluating new drilling procedures (designed to reduce drilling time to a given depth).
Notes: Drilling Engineers attempt to predict the time it will take to drill each well, and plot the predicted time vs. depth on a drilling time curve. They then compare actual depth vs. drilling time and cost to the projected. This aids in determining whether operations were carried out as planned or not.

## Slide 6: 1.5-6 Bit Weight and Rotary Speed
Increasing bit weight and rotary speed boosts drilling rate
These increases accelerate bit wear
Field tests show that drilling rate increases more or less in direct proportion to bit weight
Notes: If we reduce our drilling time, we will reduce our costs. The most obvious way that we can reduce drilling time, or increase penetration rate, is to either increase bit weight and rotary speed. This will increase penetration rate, but it also accelerates bit wear, which could actually increase cost per foot if the bit wears out prematurely, and must be replaced before the planned footage drilled
Penetration rate increases more or less in direct proportion to bit weight and rotary speed – up to a point.

## Slide 7: 1.5-7
Consider 10” hole
(don’t overdo!!)
Drilling Rate, ft/hr
Bit Weight x 1,000 lb/in
40,000 lbf
Notes: This shows the effect of bit weight on penetration rate. Penetration rate increases with bit weight until the bit starts generating more cuttings than can be efficiently cleaned from the bottom of the hole. If this happens the bit begins to flounder when the cuttings are re-ground by the bit.

## Slide 8: 1.5-8
Drilling Rate, ft/hr
Rotary Speed, RPM
Don’t overdo!
Casing wear,
bit life ...
Notes: The same is true for increasing rotary speed. Every bit is designed to operate within a specific bit weight range and rotary speed range. Pre-mature failure is a likely outcome if the upper limits are exceeded for any length of time.
To determine the “best” bit weight and rotary speed for a particular bit, the rig crew will run a drill-off test. They will record the penetration rate at incrementally higher bit weights. Once the marginal increase in penetration rate begins to decrease (the bit begins to flounder) the crew will reduce the bit weight slightly. He will then do the same with differing rotary speeds.
Keep in mind, if a directional well is being drilled, the directional driller will dictate the bit weight and rotary speed so that he can hit the target.

## Slide 9: 1.5-9
Drilling Rate, ft/hr
Hydrostatic Pressure, 1,000’s of psi
EFFECT OF BACK PRESSURE
0 - 5,000 psi
Notes: There are other factors that effect penetration that can be controlled by the rig crew. This shows the effect of increasing bottom hole pressure (really the detrimental effect that drilling overbalanced has on penetration rate). It’s pretty easy to see why drillers do not like to drill with excessive overbalance.

## Slide 10: 1.5-10
Depth, ft
Rotating Time, hours
EFFECT OF DRILLING FLUID
water vs. air
Notes: This plot shows the comparison of different drilling fluids on penetration rate. Actually this shows the increased penetration rate that one can expect from utilizing underbalanced drilling. Air drilling is much faster than drilling with water or mud.

## Slide 11: 1.5-11
EFFECT OF SOLIDS IN THE MUD
Notes: Solids free muds can increase penetration rate.

## Slide 12: 1.5-12 Hole Problems
Lost Circulation
Stuck Pipe
  Keyseat- Crooked Hole
  Differential Sticking
  Mechanical Sticking
Junk in Hole
Kicks and Blowouts
Crooked Hole
Notes: Here is a partial list of hole problems that can have a tremendous impact on drilling costs.

## Slide 13: 1.5-13 Hole Problems - Lost Circulation
Flow out < Flow in (e.g 400 < 500)
Drop in mud Return Rate
Drop in Mud Pit Volume
Blowout
Indication:
Notes: Lost circulation is the loss of whole mud to the formation. This can range from slight seepages of mud to the formation, to partial loss of returns to total loss of returns. Total loss of returns refers to an event when none of the mud pumped down the drillstring can be circulated back to the surface. It is all lost to the formation downhole. Here are some indicators of lost returns

## Slide 14: 1.5-14 Hole Problems - Lost Circulation
Poor Drilling Fluid Characteristics
Induced Fracturing of Formation From Rapid Pipe Movement
Causes:
High Formation Permeability (e.g. fractures)
Low Formation Pore Pressure
Notes: This slide shows some of the causes of lost circulation

## Slide 15
Costly Mud Makeup
Loss of Production
Fire
Loss of Permit to Drill
Results:
1.5-15 Hole Problems - Lost Circulation
Notes: This shows the results

## Slide 16: 1.5-16 Hole Problems - Lost Circulation
Preventive Measures:
Crew Education
Good Mud Program
Study Wells in Area
…to be prepared
Notes: And here are preventative measures

## Slide 17: 1.5-17 Hole Problems - Lost Circulation
Use Lost Circulation Material as Mud Additive (fibrous or granular)
Drill Through Troublesome Interval and Case Off
Decrease Mud Weight
Decrease Circulation Rate
Remedial Measures:
Notes: Finally remedial measurfes

## Slide 18: 1.5-18 Hole Problems - Stuck Pipe (drill pipe, drill collars, casing)
Indication:
Cannot Pick Up Pipe (Venezuela case)
Causes:
Cave - ins
Keyseat - Crooked Hole
Notes: Getting the drillstring stuck in the wellbore can not only be expensive and time consuming, it can also result in loss of part or all of the wellbore. The crew may have to plug back, sidetrack, and re-drill the well.
There are several causes of stuck drillpipe. In wells with borehole stability problems, cave ins can occur. If a crooked hole is drilled, the tension in the drillstring can pull the drillpipe against the inside of the bend in the hole, wearing a groove in the side of the hole. The drillpipe may be able to slide through this slot, but the larger diameter drill collars may be pulled up into this key seat when tripping out of the hole

## Slide 19
1.5-19 Hole Problems - Stuck Pipe
Differential Pressure Sticking
Filter Cake
    Deposited AFTER Circulation Stops
    - While Still on Bottom
Causes, cont’d:
Notes: Differential sticking occurs when a thick, soft, and permeable filter cake is deposited on a permeable formation when the wellbore pressure exceeds the formation pressure. If the drillstring is pushed against the walls of the hole, this differential pressure can cause the drillstring to become stuck in the side of the wellbore.
Thick filter cakes can be wiped off the walls of the hole while tripping the drillstring out of the well. This filter cake can build up on the bit enough so that it can eventually stick the drillpipe.

## Slide 20: 1.5-20 Hole Problems - Stuck Pipe
Results:
Fishing Operations
  Back off, POH, RIG w/fishing string
Loss of Hole
  or at least part of the hole
Notes: Stuck drillstring usually leads to an expensive fishing job or often loss of the hole.

## Slide 21: 1.5-21 Hole Problems - Stuck Pipe
Use Minimum Mud Weight Required to Control Formation Pressures.
Use Special Drill Collars (spiral)
Use Centralizers on Casing
Periodically Establish Circulation while Running Casing or Drillpipe in Deep Hole
Preventive Measures:
Notes: How to prevent stuck pipe

## Slide 22: 1.5-22 Hole Problems – Stuck Pipe
Erode Mud Filter Cake - at High Fluid Velocity (speed up pumps)
Spot Special Fluid; Oil, Acid
Reduce Mud Weight as Far as Possible
Rotate Pipe - Keep Moving Pipe
Remedial Measures:
If Circulation Can Be Established:

## Slide 23: 1.5-23 Hole Problems - Stuck Pipe
If Circulation Cannot Be Established:
        Cut Pipe or Unscrew Joint - and Fish
Remedial Measures:

## Slide 24: 1.5-24
KEY
SEAT
Notes: This is a diagram of the drillstring becoming stuck in a keyseat.

## Slide 25: 1.5-25
P1
P2
P1 >> P2
Notes: Differential sticking illustrated.

## Slide 26: 1.5-26
Thick Filter Cake
Thin Filter Cake
F = N
N = P A
F = P A
How is filter cake formed?
Pipe Stuck in Wall Cake
Notes: This shows that a thick soft filter cake results in a larger contact area between the pipe and the wall of the hole resulting in a larger force required to free the stuck drillpipe. The force required to free the drillstring is equal to the coefficient of friction times the normal force. The normal force is equal to the differential pressure times the contact area.

## Slide 27: 1.5-27 Hole Problems - Junk in Hole
Bit Parts Missing
Items from Surface Dropped into Hole
Erratic Torque
Indication:
Notes: Fishing jobs can result from junk in the hole. This junk can be just about anything.

## Slide 28: 1.5-28 Hole Problems - Junk in Hole
Cause:
Negligence of Crew
Result:
Fishing Operation

## Slide 29: 1.5-29 Hole Problems - Junk in Hole
Crew Education
Preventive Measure:
Remedial Measures:
Run Junk Basket
Run Basket with Collapsible Teeth (“Poor Boy” Basket)
Run Magnet
Notes: There are many tools that can be used to attempt to remove junk from the wellbore. It’s best to get a good fishing tool operator to free stuck drillpipe or retrieve junk that has been left in the hole.

## Slide 30: 1.5-30 Hole Problems - Blowout (oil, gas or water)
Returns to Surface after Circulation is Stopped (KICK!)
Well Out of Control - Big Problem!
Lost Circulation . . .
Indication:
Notes: Blowouts are the worst problem that can occur on a drilling location, and is almost always a result of human error or a series of mistakes. A blowout is the loss of control of a well, and can result in lost revenues, loss of rights to drill, environmental pollution, loss of equipment, and worst of all, injury or loss of life.

## Slide 31: 1.5-31 Hole Problems - Blowout (oil, gas or water) [surface or underground]
Causes:
Loss of Hydrostatic Head due to Lost Circulation
Poor drilling Fluid
Swabbing Effect while Pulling Drillpipe
Insufficient Mud Weight
Notes: These are really causes of kicks, which are not necessarily horrific problems, but if not recognized early, and handled correctly, can lead to a blowout.

## Slide 32: 1.5-32 Hole Problems - Blowout
Results:
Possible Loss of Life and Property
Legal and Financial Problems

## Slide 33: 1.5-33 Hole Problems - Blowout
Crew Education
Be Alert
Blowout Control Equipment on RIG including Pit Volume Indicators
Preventive Measures:
Notes: Even though in the past thirty years much has been done in the industry as far as studying well control, and in well control training, the blowout rates have remained almost flat. Why, we are constantly changing personnel, and people can always make mistakes. Auto accidents should never occur, but we still lose thousands of people every year to these accidents.
The solution – keep trained personnel on location and never let your guard down.

## Slide 34: 1.5-34 Hole Problems - Blowout
Remedial Action:
If on Bottom:
Use proper Mud Weight
Add Lost Circulation Materials
In Extreme Case of Blowout:
May Have to Directionally Drill a Relief Well
Notes: In most blowout cases, specialists should be called out to regain control

## Slide 35: 1.5-35 Hole Problems - Crooked Hole
Periodic Directional Surveys
Stuck Drill String
Casing Problems
Indication:
Notes: Very seldom are wells drilled perfectly vertically. Barring any other factors, the bit has a natural tendency to corkscrew in a clockwise direction just from the rotation of the bit. Dipping formations, drilling across faults, drilling with excessive bit weights, or too small drill collars can also cause the well path to deviate from the planned. If the dogleg is too severe, several expensive problems can be encountered.

## Slide 36: 1.5-36 Hole Problems - Crooked Hole
Causes:
Too much Weight on Bit
Dipping Formation
Anisotropic Formation
Too Small Drill Collars
No Stabilizers

## Slide 37: 1.5-37 Hole Problems - Crooked Hole
Results:
Uneven Spacing (on bottom)
Legal Problems
Production Problems
Cementing Problems

## Slide 38: 1.5-38 Hole Problems - Crooked Hole
Avoid Buckling of Drill Pipe by using sufficient number of drill collars
Use “Oversize” Drill Collars
Use Reamers and Stabilizers
Start the Hole Vertically
Preventive Action:
Notes: There are a number of things that can be done to keep the well following the planned trajectory.

## Slide 39: 1.5-39 Hole Problems - Crooked Hole
Plug Back and Sidetrack
Use Whipstock
Use Reamers in 3 Locations
Remedial Action:
Notes: In extreme cases, the wellbore may have to be re-drilled.